## Slide 1: PRNet: PAPR Reduction via Deep Autoencoder

## Slide 2: The Autoencoder Paradigm Shift
Introduced by Kim et al., PRNet is the first deep learning‐based system for joint PAPR and BER optimization. It treats the entire transceiver chain as a single deep autoencoder:
  Encoder Neural Network Transmitter
  Decoder Neural Network Receiver
  Bottleneck Noisy wireless channel
Both the transmitter and receiver are jointly trained, allowing the network to:
  Learn a custom, data‐dependent constellation mapping that jointly minimizes BER and PAPR.
  Eliminate side information (SI) overhead entirely — the decoder implicitly learns the encoder’s mapping.
  Bypass the exponential search spaces of classical methods (e.g. PTS).

## Slide 3: PRNet Transceiver Architecture
End-to-End Neural Network:
  Standard modulation and demodulation are completely replaced by a DNN Encoder and DNN Decoder.
  Structure: Input layer (128 nodes) 5 hidden layers (2048 nodes each) Output layer (128 nodes).
Inside each hidden layer block:
  Fully Connected (FC): Links all data to process subcarriers jointly.
  Batch Normalization (BN): Scales data to ensure stable and reliable training.
  ReLU Activation: Introduces the non-linearity required to solve the highly complex trade-off between PAPR and BER

## Slide 4: End-to-End System Model
Input Representation: Real I/Q vector
DNN Encoder: parameterized by weights
OFDM Mod & Channel: IFFT, then Rayleigh fading & AWGN
Demodulation & Equalization: FFT to frequency domain, zero-forcing
DNN Decoder: parameterized by weights
The Complete End-to-End Pipeline

## Slide 5: The Joint Loss Function
Reconstruction loss (MSE in):
PAPR penalty (oversampled time‐domain waveform, )
Joint loss: ( governs the BER–PAPR trade‐off)

## Slide 6: Two-Stage Training Methodology
Stage 1 — Noise Selection ( = 0): Sweep while training with reconstruction loss only.
Stage 2 —Trade‐Off Training (): Sweep penalty weight under the full loss
Denoising autoencoder: Artificial noise at a corruption level (noise‐to‐signal ratio) is injected during the forward pass to simulate the physical channel and force the decoder to learn robust decision boundaries.

## Slide 7: Simulation Setup & Parameters

## Slide 8: Learned Constellation Shaping
Unlike classical OFDM with rigid QPSK boundaries, the PRNet encoder dynamically disperses constellation points:
Maps discrete input data into a continuous, cloud-like spatial distribution.
Trades traditional Euclidean spacing for optimal PAPR reduction.
The jointly trained decoder learns to recover data from this custom distribution without explicit knowledge of the mapping.

## Slide 9: BER Performance
Original Paper
Our Reproduction
Accurate Reproduction: Our independently trained model perfectly matches the BER curve from the original paper.
Superior to Classical Methods: PRNet achieves a lower Bit Error Rate (BER) than traditional techniques like Clipping and PTS.
Proven Robustness: The results confirm that the neural network successfully learns to protect the data against severe channel fading.

## Slide 10: PAPR Performance
Original Paper
Our Reproduction
Massive Reduction: PRNet successfully reduces PAPR by an impressive 4–5 dB compared to standard OFDM (≈ 10.5 dB).
A Surprising Discrepancy: The original paper reports a final PAPR of ≈ 3 dB. However, our strict reproduction reveals the true physical PAPR is actually ≈ 6 dB.

## Slide 11: PAPR Reduction – Discrepancy Investigated
To understand why our results exactly doubled the original paper's claims, we audited the authors' open-source implementation.
  The Mathematical Impact: This coding error artificially halves the reported values, making a true 6 dB PAPR look like 3 dB.
  The Reality: Even after fixing this mathematical error, PRNet still reduces PAPR by an impressive 4–5 dB compared to standard OFDM.

## Slide 12: Computational Complexity & Limitations
Computational Complexity:
  Theoretical complexity
  Real‐time GPU inference: 480 vs. PTS: 2,890 ( 6x speedup over classical methods).
Practical Limitations of PRNet:Type equation here.
  Scalability: FC layers scale as — impractical for commercial .
  Channel mismatch: Overfits to the training fading model; degrades under unmodelled conditions.
  Configuration rigidity: Changing or requires full architectural redesign and retraining.
  Interpretability: Black‐box weights prevent worst‐case guarantees required by telecom standards.